## Slide 1: Chromatography

## Slide 2: HPTLC Workshop

## Slide 6: Different Kinds of Chromatography
Liquid chromatography (includes column chromatography, thin-layer, and HPLC)
  Stationary phase: silica, alumina, etc.
  Mobile phase (moving phase): organic solvents
  Important properties: polarity
Gas chromatography
  Stationary phase: a film of a polymer or a wax. The film must have a high boiling point
  Mobile phase: gas (Helium is the usual carrier gas)
  Important properties: boiling point

## Slide 7
Adsorption
Partition
Size Exclusion
Affinity
Ion Exchange
Liquid Chromatography
Competition between liquid mobile phase and solid stationary phase
Competition between liquid mobile phase and Liquid stationary phase
Competition between liquid mobile phase and Liquid stationary phase
Molecular
sieveing
Lock and Key Mechanism
Competition between liquid mobile phase and ionic stationary phase

## Slide 10: Thin layer Chromatography

## Slide 15: Thin-Layer Chromatography: Determination of Rf Values
Rf of component A =
dA
dS
Rf of component B =
dB
dS
The Rf value is a decimal fraction, generally only reported to two decimal places

## Slide 16: Thin-Layer Chromatography: Qualitative Analysis

## Slide 18: Horizontal Developing Chamber

## Slide 23: Visualization Method
Vizualization is a method that is used to render the TLC spots visible.
A visualization method can be:
  Ultraviolet light
  Iodine vapors to stain spots
  Colored reagents to stain spots
  Reagents that selectively stain spots while leaving others unaffected.

## Slide 27: Limitations of TLC
TLC is an open system exposed to the environmental effects like air( oxygen), climatic factors (Temperature, Humidity), Light , Fume, mechanical stress) so sensitive samples needs special care to achieve reproducible results.
Requires Manual action (Although there are computer controlled instuments available for each step but it is not feasible.
It is not suitable for Quantification.
It is not good for Biopolymer.

## Slide 28: HPTLC The State of Art - Modern equipments(Technology) - Modern Theoretical foundation(Science) - Standardized methodology(performance)

## Slide 29
This book is not intended to discredit HPLC. ndeed, it is meant for those who use HPLC. An elegant, fast, inexpensive and sufficiently recise preliminary technique for HPLC can now be provided which may be the method of choice for certain analytical problems. The technique has been named HPTLC, high performance thin-layer chromatography

## Slide 39: Important steps in HPTLC manual

## Slide 41: PRECOATED LAYERS

## Slide 42: MERCK Precoated layers for HPTLC.
034.5035
HPTLC plates cellulose F
100
10x10
25
034.5036
HPTLC plates cellulose F
100
20x10
50
034.5787
HPTLC plates cellulose (without F)
100
10x10
25
034.5786
HPTLC plates cellulose (without F)
100
20x10
25
034.5631
HPTLC plates silica gel 60 (without F)
200
10x10
25
034.5633
HPTLC plates silica gel 60 (without F)
200
10x10
100
034.5641
HPTLC plates silica gel 60 (without F)
200
20x10
50
034.3748
HPTLC plates silica gel 60 (without F), concentration zone
200
10x10
25
034.3749
HPTLC plates silica gel 60 (without F), concentration zone
200
20x10
50
034.5628
HPTLC plates silica gel 60 F 254
200
10x10
25
034.5629
HPTLC plates silica gel 60 F 254
200
10x10
100
034.5564
HPTLC plates silica gel 60 F 254 GLP
200
10x10
25
034.5642
HPTLC plates silica gel 60 F 254
200
20x10
50
034.1764
HPTLC plates silica gel 60 F 254, extra thin layer
100
20x10
25
034.3727
HPTLC plates silica gel 60 F 254, concentration zone
200
10x10
25
034.3728
HPTLC plates silica gel 60 F 254, concentration zone
200
20x10
50
034.5613
HPTLC plates silica gel 60 F 254 GLP
200
20x10
25
034.1552
HPTLC plates silica gel WR 60 F 254s
200
20x10
25
034.5445
HPTLC plates LiChrospher® Si 60 F 254s
180
20x10
25
034.5547
HPTLC aluminium sheets silica gel 60 (without F)
200
20x20
25

## Slide 43: MERCK Precoated Layers for (Conventional) TLC.
034.5713
TLC plates aluminium oxide 60 F 254
250
20x20
25
034.5718
TLC plates cellulose F
100
20x20
25
034.5716
TLC plates cellulose (without F)
100
20x20
25
034.5552
TLC aluminium sheets cellulose (without F)
100
20x20
25
034.5724
TLC plates silica gel (without F)
250
5x20
100
034.5721
TLC plates silica gel (without F)
250
20x20
25
034.1844
TLC plates silica gel (without F), concentration zone
250
10x20
25
034.1845
TLC plates silica gel (without F), concentration zone
250
20x20
25
034.5729
TLC plates silica gel 60 F 254
250
10x20
50
034.5715
TLC plates silica gel 60 F 254
250
20x20
25
034.5566
TLC plates silica gel 60 F 254 GLP
250
20x20
25
034.1846
TLC plates silica gel 60 F 254, concentration zone
250
10x20
50
034.1798
TLC plates silica gel 60 F 254, concentration zone
250
20x20
25
034.5554
TLC aluminium sheets silica gel 60 F 254
200
20x20
25
034.5553
TLC aluminium sheets silica gel 60 (without F)
200
20x20
25
034.5582
TLC aluminium sheets silica gel 60 (without F), concentration zone
200
20x20
25
034.5583
TLC aluminium sheets silica gel 60, concentration zone
200
20x20
25
034.5735
TLC plastic sheets silica gel 60 F 254
200
20x20
25
034.5748
TLC plastic sheets silica gel 60 (without F)
200
20x20
25
034.5423
TLC plates RP-18 F 254s
250
10x20
50

## Slide 44: CAMAG Adsorbents.

## Slide 45
032.3301
Aluminium Oxide CAMAG DS-0
1 kg
032.3305
Aluminium Oxide CAMAG DS-0
5 kg
032.3351
Aluminium Oxide CAMAG DS-5
1 kg
032.3355
Aluminium Oxide CAMAG DS-5
5 kg
032.3401
Aluminium Oxide CAMAG DSF-0
1 kg
032.3405
Aluminium Oxide CAMAG DSF-0
5 kg
032.3451
Aluminium Oxide CAMAG DSF-5
1 kg
032.3455
Aluminium Oxide CAMAG DSF-5
5 kg
032.3502
Cellulose, fibre type, CAMAG D-0
500 g
032.3512
Cellulose, fibre type, CAMAG DF-0
500 g
032.3552
Cellulose, microcrystalline, CAMAG DS-0
500 g
032.3562
Cellulose, microcrystalline, CAMAG DFS-0
500 g
032.1001
Silica Gel, CAMAG DS-0
1 kg
032.1005
Silica Gel, CAMAG DS-0
5 kg
032.1051
Silica Gel, CAMAG DS-5
1 kg
032.1055
Silica Gel, CAMAG DS-5
5 kg
032.1101
Silica Gel, CAMAG DSF-0
1 kg
032.1105
Silica Gel, CAMAG DSF-0
5 kg
032.1151
Silica Gel, CAMAG DSF-5
1 kg
032.1155
Silica Gel, CAMAG DSF-5

## Slide 46: MERCK Adsorbents
033.1090
Aluminium Oxide MERCK G (type 60/E)
500 g
033.1092
Aluminium Oxide MERCK GF (type 60/E)
500 g
033.1091
Aluminium Oxide MERCK G (type 60/E)
2,5 kg
033.1085
Aluminium Oxide MERCK H basic (type 60/E)
500 g
033.1094
Aluminium Oxide MERCK HF basic (type 60/E)
500 g
033.7731
Silica Gel MERCK G (type 60)
1 kg
033.7733
Silica Gel MERCK G (type 60)
5 kg
033.7730
Silica Gel MERCK GF (type 60)
1 kg
033.7729
Silica Gel MERCK GF (type 60)
5 kg
033.7736
Silica Gel MERCK H (type 60)
1 kg
033.7738
Silica Gel MERCK H (type 60)
2,5 kg
033.7745
Silica Gel MERCK HF (type 60)
500 g
033.7739
Silica Gel MERCK HF (type 60)
1 kg
033.7741
Silica Gel MERCK HF 254 + 366 (type 60)
1 kg
033.7744
Silica Gel MERCK 60 HR "high purity"
500 g
033.8129
Kieselguhr MERCK 60 G
500 g

## Slide 47: Automatic TLC Plate Coater

## Slide 48: TLC Plate Box.

## Slide 49: Drying rack

## Slide 50: Spot Application
Nanomat
Linomat
Automatic TLC Sampler

## Slide 51: NANOMAT

## Slide 52: Disposable Glass Capillaries

## Slide 53: Capillary Dispenser System

## Slide 54: LINOMAT 1V

## Slide 55: AUTOMATIC TLC SAMPLER

## Slide 57
SELECTION OF MOBILE PHASE

## Slide 58: LIGHT WEIGHT TWIN TROUGH CHAMBER

## Slide 59: Automatic Developing Chamber ADC

## Slide 60: AMD System

## Slide 61: DENSITOMETRIC CHROMATOGRAM EVALUATION

## Slide 62: TLC Scanner 3 with “CATS” Soft Ware.

## Slide 63: UV –INSPECTION -UV Lamps.

## Slide 64: POST CHROMATOGRAPHIC DERIVATIZATION
General.
Chromatogram Immersion Device.
TLC Sprayer.
Reagent Spray.
TLC Spray Cabinet.
TLC Plate Heater

## Slide 65: Chromatogram Immersion Device.

## Slide 66: TLC Sprayer.

## Slide 67: Reagent Spray.

## Slide 68: TLC Spray Cabinet.

## Slide 69: TLC Plate Heater

## Slide 70: Detection system
Some instrumental Techniques such as
    Densitometry
    Photodiode array detector
    Fluorescence
    FT-IR in ATR Mode
    Mass Spectrometric

## Slide 72: Test Dye Mixtures
032.8001
Test Dye Mixture I 100 mL (suitable for silica gel) Dimethyl yellow - Oracet blue 2R - Oracet red G; solvent: toluene
032.8002
Test Dye Mixture II 100 mL (suitable for silica gel and aluminium oxide) Sudan black - Artisil blue - Sudan yellow - fatty orange - fat red 7B - (Sudan black separates into two fractions); solvent: toluene
032.8003
Test Dye Mixture III 10 mL (suitable for HPTLC silica gel) Ciba F II - Indophenol - Ariabel red - Sudan blue II - Sudan IV - dimethylaminoazobenzene; solvent: toluene
032.8004

## Slide 100: HPTLC Advantages that must be reemphesised
Short Analysis time( severeal samples side to side( specially important in screening)
Fingerprints!!!
  (although other fingerprints also help)
Lower resolution than HPLC will not show natural variability ,will not confuse us in analysis
Multiple derivatization
Not only peak report but also image report.

## Slide 101: Major Indications in Botanicals

## Slide 114: Examples of Using HPTLC In Quality control of Botanicals

## Slide 119: Bioautography

## Slide 133: DIFFERENCES BETWEEN TLC AND HPTLC

## Slide 134
PARAMETER | TLC | HPTLC
Type of chromatographic plates | Hand made/pre coated | Pre coated
Absorbant layer | 200-250mm | 100-150mm
Particle size | 5-20 micrometer | 4-8 micrometer
Application of sample | Manual/semi automatic | Semi automatic
Shape of sample | spot | band

## Slide 135
Spot size | 3-6mm | 1-2mm
Sample volume | 1-10 microlit | 0.1-2microlit
No of sample per plate | 15-20 | 40-45
Optimal development distance | 10-15cm | 5-7cm
Development time | Depend upon mobile phase | 40% less than TLC
Quantization | Manual | Manual/ instrumentation
Reproducibility of result | difficult | Reproducible

## Slide 137: Reprostar.

## Slide 138: Video store.

## Slide 139: OPTIMIZATION OF DEVELOPING CONDITION.
HPTLC VARIO SYSTEM.